Disclaimer

- Purpose – This Guide has been produced by the Australian Energy Market Operator Limited (AEMO) to provide information about Generator technical requirements and NEM registration, as at the date of publication.

- No substitute – This Guide is not a substitute for, and should not be read in lieu of, the National Electricity Law (NEL), the National Electricity Rules (Rules) or any other relevant laws, codes, rules, procedures or policies. Further, the contents of this Guide do not constitute legal or business advice and should not be relied on as a substitute for obtaining detailed advice about the NEL, the Rules, or any other relevant laws, codes, rules, procedures or policies, or any aspect of the national electricity market or the electricity industry.

- No Warranty – While AEMO has used due care and skill in the production of this Guide, neither AEMO, nor any of its employees, agents and consultants make any representation or warranty as to the accuracy, reliability, completeness or suitability for particular purposes of the information in this Guide.

- Limitation of liability - To the extent permitted by law, AEMO and its advisers, consultants and other contributors to this Guide (or their respective associated companies, businesses, partners, directors, officers or employees) shall not be liable for any errors, omissions, defects or misrepresentations in the information contained in this Guide, or for any loss or damage suffered by persons who use or rely on such information (including by reason of negligence, negligent misstatement or otherwise). If any law prohibits the exclusion of such liability, AEMO’s liability is limited, at AEMO’s option, to the re-supply of the information, provided that this limitation is permitted by law and is fair and reasonable.

© 2010 - All rights reserved.

| Name of person applying for registration as a Generator: | [insert company name and ABN] |
| --- | --- |
| Network Service Provider: | [insert company name and ABN of NSP] |
| Name of generating system: | [insert name of power station, wind farm or other generating system] |
| Generating unit designations: | [insert unit designations eg Units 1 to 4] |
| Generating unit Rated MW (Generated) | [insert unit “Rated MW (Generated)” as defined in Schedule S5.5.1] |
| Connection point voltage: | [insert connection point voltage or voltages if more than one] |

Please complete the following table confirming compliance with the requirements of Chapter 5 of the National Electricity Rules by indicating in the Compliance column your Rules Compliance, Connection Agreement Compliance or whether the clause is not relevant in this situation. Comments are also required in some areas where a compliance statement is not. Please note that shaded areas do not require completion and are included for ease of reading or for the information of Applicants who will need to comply as applicable.

Please note the following items should also be submitted with this document:

- The Generator Performance Standards and Generating Unit Design Data documents also available from AEMO’s website

- A control system block diagram

5.	Network Connection

| CLAUSE | CLAUSE TEXT | COMMENT | COMPLIANCE |
| --- | --- | --- | --- |
| 5.2.5 | Obligations of generators |  |  |
| 5.2.5 (a) | Each Generator must plan and design its facilities and ensure that its facilities are operated to comply with: |  |  |
|  | (1) its connection agreement with a Network Service Provider; |  |  |
|  | (2) subject to clause 5.2.5(a)(1), all applicable performance standards; and |  |  |
|  | (3) subject to clause 5.2.5(a)(2), the system standards. |  |  |
| 5.2.5 (b) | A Generator must: |  |  |
|  | (1) submit an application to connect in respect of new or altered equipment owned, operated or controlled by the Generator and enter into a connection agreement with a Network Service Provider in accordance with clause 5.3 prior to that equipment being connected to the network of that Network Service Provider or altered (as the case may be); |  |  |
|  | (2) comply with the reasonable requirements of the relevant Network Service Provider in respect of design requirements of equipment proposed to be connected to the network of that Network Service Provider in accordance with clause 5.4 and schedule 5.2; |  |  |
|  | (3) provide generation forecast information to the relevant Network Service Provider in accordance with clause 5.6; |  |  |
|  | (4) permit and participate in inspection and testing of facilities and equipment in accordance with clause 5.7; |  |  |
|  | (5) permit and participate in commissioning of facilities and equipment which are to be connected to a network for the first time in accordance with clause 5.8; |  |  |
|  | (6) operate its facilities and equipment in accordance with any direction or clause 4.8.9 instruction given by AEMO; and |  |  |
|  | (7) give notice of intended voluntary permanent disconnection in accordance with clause 5.9. |  |  |

| SCHEDULE 5.2 CONDITIONS FOR CONNECTION OF GENERATORS |
| --- |
| SCHEDULE | SCHEDULE TEXT | COMMENT | COMPLIANCE |
| S5.2.1 | Outline of requirements |  |  |
| S5.2.1 (a1) | The equipment associated with each generating unit must be designed to withstand without damage the range of operating conditions which may arise consistent with the system standards. |  |  |
| S5.2.1 (a2) | Generators must comply with the performance standards and any attached terms or conditions of agreement agreed with the Network Service Provider or AEMO in accordance with a relevant provision of schedules 5.1 or 5.1a. |  |  |
| S5.2.2 | Application of settings |  |  |
|  | A Generator must only apply settings to a control system or a protection system that are necessary to comply with performance requirements of this schedule 5.2 if the settings have been approved in writing by the relevant Network Service Provider and, if the requirement is one that would involve AEMO under clause 5.3.4A(b) of the Rules, also by AEMO. A Generator must not allow its generating unit to supply electricity to the power system without such prior approval. |  |  |
|  | If a Generator seeks approval from the Network Service Provider to apply or change a setting, approval must not be withheld unless the Network Service Provider or, if the requirement is one that would involve AEMO under clause 5.3.4A(b) of the Rules, AEMO, reasonably determines that the changed setting would cause the generating unit to not comply with the relevant performance standard or cause an inter-regional or intra-regional power transfer capability to be reduced. |  |  |
|  | If the Network Service Provider or, if the requirement is one that would involve AEMO under clause 5.3.4A(b) of the Rules, AEMO, reasonably determines that a setting of a generating unit's control system or protection system needs to change to comply with the relevant performance standard or to maintain or restore an inter-regional or intra-regional power transfer capability, the Network Service Provider or AEMO (as applicable) must consult with the relevant Generator, and the Network Service Provider may request in writing that a setting be applied in accordance with the determination. |  |  |
|  | The Network Service Provider may also request a test to verify the performance of the relevant plant with the new setting. The Network Service Provider must provide AEMO with a copy of its request to a Generator to apply a setting or to conduct a test. |  |  |
|  | A Generator who receives such a request must arrange for the notified setting to be applied as requested and for a test to be conducted as requested. After the test, the Generator must, on request, provide both AEMO and the Network Service Provider with a report of a requested test, including evidence of its success or failure. Such a report of a test is confidential information. |  |  |
|  | A Generator must not change a setting requested by the Network Service Provider without its prior written agreement. If the Network Service Provider requires a Generator to change a setting within 18 months of a previous request, the Network Service Provider must pay the Generator its reasonable costs of changing the setting and conducting the tests as requested. |  |  |
| S5.2.4 | Provision of information |  |  |
| S5.2.4 (a) | The Generator must promptly on request provide all data of the kinds specified in schedule 5.5 reasonably required by AEMO or the Network Service Provider. |  |  |
| S5.2.4 (b) | Three months before first synchronisation a Generator must, in respect of each proposed scheduled generating unit, provide AEMO and the relevant Network Service Provider and any relevant Distribution Network Service Provider with the following information about the generating unit’s control systems for frequency control and voltage control: |  |  |
|  | (1) a set of functional block diagrams, including all functions between feedback signals and generating unit output; |  |  |
|  | (2) the parameters of each functional block, including all settings, gains, time constants, delays, deadbands and limits; and |  |  |
|  | (3) the characteristics of non-linear elements, |  |  |
|  | sufficient for AEMO and the relevant Network Service Provider to perform short and long-term simulation studies. |  |  |
|  | The information provided must be updated within 3 months after commissioning tests or other tests undertaken in accordance with clause 5.7.3 of the Rules are completed. The connection agreement must record the process for subsequently changing this information. Conformance with the requirements described in this clause is the responsibility of the Generator and is subject to the provisions of clause 5.7.3(f) of the Rules for each generating unit. |  |  |