## Slide 1: 5MS Joint Metering/Systems Focus Group
Friday, 14 September 2018
AEMO Office:
Level 22, 530 Collins Street, Melbourne

## Slide 2: Agenda
NO |  | Time | AGENDA ITEM | Responsible
Preliminary Matters |  |  |  | 
1 | 9:30am – 9:40am | 9:30am – 9:40am | Welcome, introduction and apologies | Emily Brodie (AEMO)
Matters for Noting |  |  |  | 
2 | 9:40am – 9:50am |  | AEMO’s profiling of 15 and 30-minute data | David Ripper (AEMO)
3 | 9:50am – 10:00am |  | Unit of measure precision | Hamish McNeish (AEMO)
4 | 10:00am – 10:10am |  | AEMO use of B2M (MDFF format) | Hamish McNeish (AEMO)
5 | 10:10am – 10:20am |  | Extending NEM12 to include 5-minute data | David Ripper (AEMO)
 | 10:20am – 10:30am |  | Break | 
Matters for Discussion |  |  |  | 
6 | 10:30am – 11:00am |  | Accepting non-settlement data | Hamish McNeish (AEMO)
7 | 11:00am – 1:00pm (includes lunch break) |  | Transition to 5-minute meter data AEMO program schedule Aggregating and profiling metering data How will participants deal with metering data during transition Develop high level milestones for key activities | David Ripper and Hamish McNeish (AEMO)
8 | 1:00pm – 1:30pm |  | File size and communications capabilities | Feedback from participants
Other business |  |  |  | 
9 | 1:30pm – 1:50pm |  | General questions | David Ripper and Hamish McNeish (AEMO)
10 | 1:50pm – 2:00pm |  | Next steps | David Ripper and Hamish McNeish (AEMO)

## Slide 3: Attendees
Name | Company / Department | Name | Company / Department
Emily Brodie | AEMO | Andy Gillis | ETSA Utilities
Blaine Miner | AEMO | Jeff Roberts | Evoenergy
Lee Brown | AEMO | Divya Kapoor | Flow Power
David Ripper | AEMO | Gaurav Ganve | Harmonic Analytics
Craig Shelley | AEMO | Victor Sanchez | Infigen
Hamish McNeish | AEMO | Ty Crowhurst | IntelliHub
Umesh Dutt | AEMO | Rajiv Balasubramanian | Jemena Limited
Mark Riley | AGL Energy Limited | Jonathon Briggs | Metering Dynamics
Paul Willacy | Aurora Energy | Jackie Mayo | Metering Dynamics
Alex Polonetskiy | Ausgrid | Eric Januar | Momentum Energy
Mahdi Maleki | AusNet | Mario Iogha | Origin Energy Limited
Dino Ou | Endeavour Energy | Mark Pilkington | Powercor
Rahman Qazi | Endeavour Energy | Justin Stute | Select Data and Measurement Solutions
Enrico Buenaventura | Energy Australia Pty Ltd | Aakash Sembey | Simply Energy
Andrew Markwell | ERM Power Limited | Paul Greenwood | Vector Advanced Metering Services (Australia) Pty Ltd
Tim Lloyd | Essential Energy |  | 

## Slide 4: AEMO’s profiling of 15 and 30-minute data
David Ripper

## Slide 5: Profiling of 15 and 30-minute meter data
Question
How will AEMO undertake profiling?
Outcome
AEMO will profile from 15 minute to 5 minute and 30 minute to 5 minute using a percentage allocation method
The profiling at the moment is at the profile area
If Global Settlement drives changes then we will take this into account

## Slide 6: Profiling – percentage allocation method
Example
5 minute trading interval (TI) | 1 | 2 | 3 | 4 | 5 | 6 | Total for 30 minutes
Wholesale feeder TI values | 100 | 150 | 120 | 150 | 230 | 250 | 1000
TI value % of 30 minute total | 10% | 15% | 12% | 15% | 23% | 25% | 100%
Corresponding 30 minute TI | 10 |  |  |  |  |  | 
5 minute trading interval (TI) | 1 | 2 | 3 | 4 | 5 | 6 | Total for 30 minutes
30 minute TI profiled to 5 minute | 10 x 10% | 10 x 15% | 10 x 12% | 10 x 15% | 10 x 23% | 10 x 25% | 
5-minute profile values | 1 | 1.5 | 1.2 | 1.5 | 2.3 | 2.5 | 10

## Slide 7: Profiling of 15 and 30-minute meter data
Topic Outcomes:
General acceptance of proposed profiling methodology
Questions/discussion included:
  Profiling is imperfect but the proposed approach seems reasonable
  How would mixed meter types under a single NMI be treated under this proposal?
  Would 5 minute meter data be peeled off prior to profiling occurring? Answer - Yes
  Is this approach representative enough for non-5 minute meters?
  Profiling impacts would be predominantly limited to the transitional period where 5 minute meters are being rolled-out
Actions:
  AGL to provide their issues/concerns regarding proposed methodology and suggest alternative (if possible)
  MDPs to provide information, detailing the type and number of instances, where mixed metering scenarios are occurring in the market today
  AEMO to consider implications of mixed metering scenarios on the proposed profiling methodology

## Slide 8: Unit of measure precision
Hamish McNeish

## Slide 9: Precision of kWh Meter Reads
Question
A concern was raised on possible loss of precision if AEMO stores meter reads in kWh. For example receiving a value of 3.2 Watt-hours.
Outcome
MDFF NEM12 and NEM13 formats currently define support to 1 Wh precision.
MDMF support is assumed to be the same – but the format is not explicit
AEMO could support to 4 decimal places and update the formats
AEMO’s systems would convert received meter reads to kWh supporting up to 4 decimal places
AEMO’s systems would accept Wh, kWh, MWh, and the stored value would be to 4 decimal places in kWh, rounding would occur if required.
Other units of measure will be treated consistently, such as for vars

## Slide 10: Unit of measure precision
Topic Outcomes:
Proposed approach, 4 decimal places in kWh, was supported
Questions/discussion included:
  4 decimal place accuracy requirement mainly relevant to unmetered loads
  AGL noted that the gas procedures provided guidance on how to round and when to round.
  Powercor noted that the proposed level of precision was greater than the accuracy of the metering fleet.
Actions:
  AEMO to propose rounding methodology that is consistent with gas procedures

## Slide 11: AEMO use of B2M (MDFF)
Hamish McNeish

## Slide 12: To-Be Process – MDFF delivery
Green is existing and unchanged, Orange is new
MDFF will be accepted over web API’s and FTP

## Slide 13: MDFF vs MDMF
Supporting of 5 minute meter data
  MDFF - Supports different intervals in the format
  MDMF - Does not support different intervals – required to be 30-minute
Options:
  Option A: Use MDMF – change format and/or add interval to standing data
  Option B: Use MDFF – already supports 5 minute
Current SWG and PWG discussion supported Option B.

## Slide 14: Meter Data over B2B and B2M
Data Formats will unify to MDFF
Participants may use MDMF to send interval reads (N1 or signed E1/B1 etc) @ 30-min resolution (or) consumption for Basic meters
Participants may use MDFF to send interval reads (E1, E2, B1, K1, Q1 etc) @ 5-min or 15-min or 30-min resolution (or) consumption for Basic meters
Validation:
  PMD/VMD B2B processes remain unchanged
  For B2M meter data AEMO proposes to periodically run the RM11 report to inform MDP’s of missing meter reads
  RM11 could be delivered prior to 1 July 2020. Is this wanted? And when?

## Slide 15: AEMO use of B2M (MDFF)
Topic Outcomes:
Agreement in principle regarding AEMO transitioning to MDFF
Concerns raised regarding how MDFF would be able to support current AEMO validation requirements for basic meter reads
Automated AEMO initiated RM11 viewed favourably
Questions/discussion included:
Discussion regarding the benefits of AEMO becoming a B2B participant i.e. allows for more streamlining of the process and limits the changes to be made to MDP systems
How can MDFF support current AEMO MDM validation requirements?
Bringing basic meter reads into MDFF via B2M for AEMO was seen as a worse outcome than keeping things status quo
Focus of moving to MDFF needs to be reconsidered in light of validation issues/concerns
Concerns regarding the potential mis-match between market participant and AEMO validation requirements for basic meter reads
Actions:
  AEMO to circulate current basic meter validation rules
  Participants to detail issues associated with supporting current AEMO basic meter validations in MDFF
  AEMO to decide if and how it may leverage B2B processes

## Slide 16: Extending NEM12 to include 5-minute data
David Ripper

## Slide 17: NEM12 to include 5-minute data
No comments received on needing an additional data format
NEM12 format can support 5-minute data with out a format change
Interval length to remain in 200 record
The MDFF document will be updated with how the 5-minute reads will be represented
Changes identified in the HLIA
  Add in AEMO to list of parties to receive MDFF
  Interval metering data – add 5-minute data to section 3.3.3.
  Define 5 minute start and end times.
  Remove MDM and net data file references.
  Produce example of 5 minute file.
    300 record [288 interval values for 5 minute, 96 interval values for 15 minute, 48 interval values for 30 minute]

## Slide 18: Proposed NEM12 Examples
Current 300 record
300,20040201,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,A,,,20040202120025,20040202142516
Proposed 300 record
300,20040201,[288 interval values for 5 minute, 96 interval values for 15 minute, 48 interval values for 30 minute],A,,,20040202120025,20040202142516

## Slide 19: Extending NEM12 to include 5-minute data
Topic Outcomes:
Agreement that the Interval Length value should remain in the 200 record of MDFF
Agreement that intraday interval length changes should not be permitted
  MDP has to aggregate the day 1 data for a meter exchange to the original interval length
Definition of 5 minute interval (start and end time) should align with the dispatch definition
Proposed NEM12 examples accepted
Questions/discussion included:
  Simply Energy raised the potential of moving the Interval Length field to the Header/100 record to allow for greater processing efficiency
  An alternative discussed suggested that maybe only allowing 1 interval length in a file may be beneficial
  Overall there was a view that changing the interval length from the 200 record was counter intuitive e.g. likely lead to an increase in the number of files
  Vast majority of participants wanted the current approach retained
  Items to be included in the procedural changes
    Intraday interval length changes are not acceptable so meter churn MDP has to aggregate the day 1 change to the original interval length i.e. 15 or 30 minutes (so that one interval length for a day in maintained)
    When defining 5 minute interval (start and end time) ensure that it is aligned with the dispatch interval definition
    Proposed examples accepted in general but a request was made to have at least 1 complete five minute (288 periods), 15 minute (96 periods) and 30 minute (48 periods) example in the MDFF Spec, other scenarios could be the proposed cutdown approach
    Ensure “allowed interval length” includes 5 minute
    Review MDFF Clarifications document to ensure MDFF Specification includes the clarifications, then remove clarifications document

## Slide 20: Accepting non-settlement data
Hamish McNeish

## Slide 21: Non-settlement data
With a view of future-proofing AEMO will add capability to handle accepting non-energy settlement streams. So if this data is provided in MDFF and registered in standing data then AEMO’s systems will support this. On the horizon:
  3rd Party Access to Data (Customer Data Right)
  Settling Virtual Power Plants
  Support of Distributed Energy Resources (DER) services
The MDM will need to determine which data streams provided via MDMF/MDFF will be accepted, validated, made available and used in settlement.

## Slide 22: Data streams treatment – UOM and sign
The MDM requires a means to determine the unit of measure of received meter data:
  Option 1: Use MDFF Record 200 – validate UOM is of a known type. Data streams via MDMF received data are always in kWh.
  Option 2: Addition to standing data (CNDS), and validate that the NEM12/13 content matches this.
The MDM requires a means to identify if the usage sent in MDFF should be treated as a positive or negative: (MDMF is always signed)
  Option 1: Using the first character of data stream suffix (e.g. ‘E’ is Export, ‘B’ is Import etc)
  Option 2: New attribute to indicate whether the data stream (or register) is Import (B1) or Export (E1) or Signed (N1) in CNDS

## Slide 23: Data streams treatment – accepting
With receipt of additional data streams (non-settlement) how should this be registered?
  Option 1: Only settlement data streams are registered in CNDS
  Option 2: All data streams are registered in CNDS and validated, a new field indicates those to be used in settlement
  Option 3: Use other existing attributes of CNDS, like Data stream Type, First character of suffix etc
Related to Option 2, there is the possibility of AEMO receiving of meter data for a data stream that isn’t currently registered and waiting a period of time for the data stream to be registered, and to then load that parked metering data.
  If not resolved in X (3?) days then the read becomes invalid and would be rejected
  These “missing” reads would not show up in the RM11 since the data stream has not been defined
  A new report may be required to highlight these reads in a parked state in need of a data stream definition

## Slide 24: Accepting non-settlement data
Topic Outcomes:
UOM specified in the MDFF 200 record will be validated against known UOM types
Application of data i.e. signage to be derived based on the first character of the data stream suffix
Only settlement data streams are to be registered in the CNDS/Data Stream table
No decision made regarding how long meter data should be stored where standing data is not present
Questions/discussion included:
Concerns were raised about introducing any new Data stream Table fields as a validation mechanism for meter read inclusion
AEMO confirmed that current validations looks at the Data Stream Type field (C or I)
No settlement value in including new standing data fields in the Data stream table
Discussion regarding perceived duplicate efforts regarding Data Stream and Register table maintenance
Views varied regarding how long AEMO should store meter reads where no standing data exists
Actions:
Participants to provide context for why AEMO should retain meter data, where required standing data does not exist, for longer than 15 days

## Slide 25: Transition to 5-minute data
David Ripper and Hamish McNeish

## Slide 26: AEMO program schedule
AEMO accepts MDFF files from 1 July 2020 – and will settle with these
AEMO expects participant to send either MDMF or MDFF for a data stream – not both
Only MDMF retrospective net reads will be accepted from 1 July 2022
MDMF format will no longer be accepted after 1 July 2023
Participants have a 3 year period from 1 July 2020 to transition from MDMF to MDFF (noting only retrospective reads supported in the last year)

## Slide 27: Aggregating and profiling metering data
Before 1 July 2020 – MDPs will need to aggregate 5 and 15 minute to 30 minute and provide in MDMF format to AEMO for settlement
Before 1 July 2020 – Participants and MDPs may choose to exchange new 5 and 15 minute data via B2B
From 1 July 2020 – 5 and 15 minute reads received by AEMO will be aggregated by AEMO to 30 minutes and settled
From 1 July 2021 AEMO will profile received 30 and 15 minute reads to 5 minute resolution
From 1 July 2022 AEMO will only accept retrospective reads via MDMF files
From 1 July 2023 AEMO will reject or ignore any received MDMF files

## Slide 28: How will participants deal with metering data during transition?
AEMO will support MDMF for a 2 year window after 1 July 2021
Participants will need to manage the handling of different resolution data and formats (from MDPs) during the transition periods.
Participants may have additional data stream standing data (CNDS) to provide/modify when 5 minute support is introduced
Metering data delivered via B2B and delivery of metering data to AEMO (MDMF and MDFF) are independent
If a newer version of meter data exists it is required to be delivered to participants and AEMO

## Slide 29: Develop high level milestones for key activities
Activity:
  Group discussion and whiteboard use to identify key milestones
Proposed Areas to Cover:
  Timeframe 1 Dec 2019 to 1 Jul 2023
  Approx. 23,500 meters to transition by 1 July 2021 (Type 1,2,3,7, subset of Type 4)
  New and replacement meters
    From Dec-18, any new or replacement meters other than Type 4A must be 5 minute capable
    From Dec-19, any new or replacement Type 4A must be 5 minute capable
    By Dec-22, all meters installed under 1. and 2. above must be producing 5 minute data
  Meter reconfiguration program
  CATS aseXML schema/standing data
  Meter data sending/receipt capability
  Participant types: MDPs, AEMO, DBs, Retailers, MC, MPB
Outcomes:
  Proposed high-level milestone dates

## Slide 30: Transition to 5-minute data
Topic Outcomes:
The Rules allows for the delivery of 5 minute meter data prior to 1 July 2021
Overall sentiment was that no participants would be ready for any 1 July 2020 production activities
A soft start of 31 March 2021 was suggested by AGL, to mitigate 1 July 2021 risks
Questions/discussion included:
What are the risks of a ‘big bang’ on 1st July 2021?
How do we manage some participant(s) not being ready by 1 July 2021?
AEMO suggested that 1 July 2020 start would be valuable in supported two 30 week settlement cycles prior to go-live
Concerns raised about being able to install 5 minute meters prior to rule implementation date – NER 7.10.5 MDP can collate metering data in sub-multiples of a trading interval with agreement of the LNSP, AEMO and FRMP.
Risk of market settlement inaccuracies occurring if 5MS was not implemented correctly
There was a suggestion to have a soft start go-live of 31 March 2021 to mitigate 1 July 2021 fall over risk
There were concerns that even 31 March 2021 would be challenging and that a strong commitment is needed by all Market Participants for this to occur
Benefits of creating a Transition Working Group was discussed
Actions:
Participants to provide information regarding transition activities and milestones by 28 Sept
  Activities and milestones to specifically include: Delivery and reception of 5 minute meter data and Connection to AEMO systems

## Slide 31: File size and communications capabilities
Hamish McNeish

## Slide 32: 1 MB Message File size
Reduce overall growth in number of files
There is support in the SWG and PWG to increase the current B2B and B2M 1 MB message content (uncompressed) limit.
AEMO is assessing:
  What we believe our systems and networking can cope with and maintain service levels
  Review current archiving services of messages (with 13 months online currently)
Due to the increase in received data (regardless of the 1 MB limit) AEMO is assessing:
  The potential need to increase bandwidth allocations, and AEMO’s network infrastructure
  Costs of bandwidth allocations
Questions
Do participants support increasing for both B2B and B2M?
What are attendees system constraints?
What size should we increase to? 5/10/X MB has been proposed as a possible target

## Slide 33: File size and communications capabilities
Topic Outcomes:
File size analysis has not been completed yet so agreement could not be reached at this stage
Questions/observations included:
Some MDPs advised that file sizes up to 10 MB were suitable, while still being able to handle the frequency, bandwidth and processing
DBs, MPs suggested that 10 MB could be too big for transaction processing and meeting SLAs
Actions:
AEMO and participants to conduct file size analysis, including any system/infrastructure constraints, and provide options for discussion

## Slide 34: Summary of Actions
Item | Workshop Section | Action | Responsible | Due Date
1 | Profiling of 15 and 30-minute meter data | AGL to provide their issues/concerns regarding proposed methodology and suggest alternative (if possible) | AGL | Fri 28 Sept 2018
2 | Profiling of 15 and 30-minute meter data | MDPs to provide information, detailing the type and number of instances, where mixed metering scenarios are occurring in the market today | MDPs | Fri 28 Sept 2018
3 | Profiling of 15 and 30-minute meter data | AEMO to consider profiling implications of mixed metering scenarios once information from MDPs is received | AEMO | Fri 5 Oct 2018
4 | Unit of measure precision | AEMO to propose rounding methodology that is consistent with gas procedures | AEMO | Fri 28 Sept 2018
5 | AEMO use of B2M (MDFF) | AEMO to circulate current basic meter validation rules | AEMO | Fri 28 Sept 2018
6 | AEMO use of B2M (MDFF) | Participants to detail issues associated with supporting current AEMO basic meter validations in MDFF | All participants | Wed 3 Oct 2018
7 | AEMO use of B2M (MDFF) | AEMO to decide if and how it will utilise B2B processes | AEMO | Wed 3 Oct 2018
8 | Accepting non-settlement data | Participants to provide context for why AEMO should retain meter data, where required standing data does not exist, for longer than 15 days | All participants | Wed 3 Oct 2018
9 | Transition to 5-minute data | Participants to provide information regarding transitional activities and milestones Activities and milestones to specifically include: Delivery and reception of 5 minute meter data and Connection to AEMO systems | All participants | Fri 12 Oct 2018
10 | File size and communications capabilities | AEMO and participants to conduct file size analysis, including any system/infrastructure constraints, and provide options for discussion | AEMO and all participants | Wed 21 Nov 2018

## Slide 35: General questions
David Ripper and Hamish McNeish

## Slide 36: Next steps
David Ripper

## Slide 37: Next steps – procedures consultation
Consultation will proceed for metering data package of procedures
Procedure Title | Consultable Procedure | Impact
MDFF Specification NEM12 and NEM13 | N | High
MSATS Procedure: Metering Data Management (MDM) Procedure | Y | High
MDM File Format and Load Process | N | Medium
Metrology Procedure: Part A | Y | High
Metrology Procedure: Part B | Y | High
Retail Electricity Market Glossary and Framework | Y | High