## Slide 1: ST PASA Replacement Project
Industry Update (Dec 2020)

## Slide 2: Agenda
The ST PASA Replacement Project
  Objective & Progress to date
Proposed HLD
  Key Themes
  System Design
  Determination of Reliability
  Benefits of the Proposed Approach
Proof of Concept
  Forecasting at nodal level
  Accounting for uncertainty
  The optimiser
  Work Still In Progress
    LOR Levels
    Run types
    Frequency of runs
    Display
    Other topics
Next Steps
Communication with AEMO

## Slide 3: ST PASA Replacement Project
Objective: To do a holistic review of the PD/ST PASA methodology and develop a system that would serve the NEM now, and into the future.
Progress to date:
AEMO engaged Intelligent Energy Systems (IES) & Steve Wallace Advisory (SWA) to assist with
Industry consultation
Review of international practices
Survey off-the-shelf IT solutions available
Publication of report including
Business requirements
High level design (HLD)
Link to ST PASA Webpage
The project team is in the middle of the development of a
Proof of Concept
Draft Rule Change proposal

## Slide 4: Key themes of HLD
Reliability is a physical system issue hence the model should reflect the physical reality instead of the market
  Full network model
  Forecast at nodal level (load on bus)
Determine uncertainties in demand forecast, VRE forecasts and scheduled unit forced outages
  They become an input into the model (known as ‘Uncertainty Margins’)
Better energy storage models
Identify system security issues like low inertia, system strength etc
Suggest lowest cost RERT activation schedules, if required

## Slide 5: Proposed PD/ST PASA System

## Slide 6: Determination of Reliability – the new paradigm
 | Current ST PASA | Proposed System
Objective | Create generation profile that maximises reserve by maximising supply to RRN | Create generation profile that meets the demand at each node
Subject to | n-1 security constraints for predefined network configurations (Transmission contingencies only) | n-1 security constraints for any network configuration and set of contingencies (Transmission and generator contingencies)
Demand Used | 50% POE demand | 50% POE demand + Uncertainty Margin
Reliability Measure | Reserve = Gen – 50% POE Demand | Deficit = Uncertainty Margin + 50% POE Demand - Gen
LOR Declared | LOR 3 if Reserve < 0 LOR 2 if Reserve <= LOR 2 level LOR 1 if Reserve <= LOR 1 level LOR2/1 level = Max (LCR/LCR2, FUM) where LCR represents either a generator or interconnector contingency | Deficit > 0 The three LOR levels are discussed later in the presentation Note: Since the generator contingencies are already considered while creating a gen profile they cannot be used as a method for determining the different levels of LOR

## Slide 7: Determination of Reliability – the new paradigm
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48
Gen Profile | 9484.05 | 9528.13 | 9467.41 | 9391.13 | 9344.2 | 9326.2 | 9306.4 | 9274.84 | 9271.06 | 9301.57 | 9343.77 | 9387.74 | 9447.78 | 8974.2 | 9058.95 | 9063.11 | 9085.59 | 9117.14 | 9070.88 | 9024.27 | 9062.78 | 9084.74 | 9010.7 | 8977.56 | 9058.83 | 9163.61 | 9229.49 | 9345.48 | 9371.66 | 9375.47 | 9488.8 | 9508.87 | 9925.95 | 10238.84 | 10246.07 | 10255.42 | 10275.12 | 10251.06 | 10319.17 | 10327.63 | 10322.03 | 10352.32 | 10412.75 | 10111.53 | 10109.17 | 9783.67 | 9722.5 | 9698.49
50 POE Demand | 6681 | 6479 | 6345 | 6245 | 6166 | 6092 | 6037 | 6010 | 5994 | 6026 | 6065 | 6173 | 6243 | 6432 | 6602 | 6811 | 6920 | 6965 | 6984 | 7045 | 7096 | 7244 | 7435 | 7594 | 7787 | 7983 | 8164 | 8349 | 8556 | 8742 | 8949 | 9156 | 9368 | 9478 | 9585 | 9579 | 9506 | 9366 | 9342 | 9268 | 9088 | 8865 | 8577 | 8230 | 7904 | 7587 | 7321 | 7005
FUM | 641.8 | 644.6 | 647.4 | 650.1 | 652.9 | 655.6 | 658.1 | 660.7 | 663.3 | 665.7 | 667.8 | 669.7 | 671.4 | 673 | 674.5 | 676 | 677.3 | 678.4 | 679.5 | 666.9 | 660 | 663.9 | 668 | 668.6 | 669.3 | 670 | 670.7 | 667.9 | 661.5 | 655 | 648.5 | 638.5 | 632.1 | 625.8 | 619.6 | 617 | 621.7 | 630.1 | 638.4 | 646.6 | 658.9 | 671.6 | 680.6 | 685.1 | 686 | 691.3 | 700.9 | 706.3
LOR1 Level | 1155 | 1155 | 1155 | 1155 | 1155 | 1155 | 1155 | 1155 | 1155 | 1155 | 1155 | 1155 | 1154.9999 | 1155 | 1155 | 1155 | 1155 | 1155 | 1144 | 1122 | 1103 | 1086 | 825.5072 | 700 | 700 | 700 | 700 | 700 | 700 | 700 | 700 | 705.9024 | 700 | 700 | 700 | 700.0001 | 700 | 700 | 722.1095 | 700 | 700 | 737.2271 | 1085 | 1085 | 1085 | 1155 | 1155 | 1155
LOR2 Level | 720 | 720 | 720 | 720 | 720 | 720 | 720 | 720 | 720 | 720 | 720 | 720 | 719.9999 | 720 | 720 | 720 | 720 | 720 | 720 | 720 | 720 | 720 | 474.5072 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 352.9512 | 350 | 350 | 350 | 350.0001 | 350 | 350 | 361.0548 | 350 | 350 | 372.2271 | 720 | 720 | 720 | 720 | 720 | 720
LOR Reserve | 2802.91 | 3049.18 | 3122.69 | 3146.61 | 3177.95 | 3234.36 | 3269.06 | 3264.42 | 3277.06 | 3275.93 | 3278.27 | 3214.79 | 3204.74 | 2542.61 | 2456.23 | 2252.57 | 2165.88 | 2152.09 | 2087.33 | 1979.68 | 1966.89 | 1840.56 | 1575.51 | 1383.37 | 1271.98 | 1180.9 | 1065.34 | 996.17 | 815.87 | 633.15 | 540.05 | 352.95 | 558.45 | 761.02 | 660.93 | 676.33 | 769.53 | 884.74 | 977.6 | 1059.71 | 1234.4 | 1487.23 | 1835 | 1881.38 | 2205 | 2196.68 | 2401.84 | 2693.13
Current STPASA
Proposed System
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48
50 POE Demand + UM(90) | 6081 | 5879 | 5745 | 5645 | 5566 | 5492 | 5437 | 5410 | 5394 | 5426 | 5465 | 5573 | 5643 | 5832 | 6002 | 6211 | 6320 | 6365 | 6384 | 6445 | 6496 | 6644 | 6835 | 6994 | 7187 | 7383 | 7564 | 7749 | 7956 | 8142 | 8349 | 8556 | 8768 | 8878 | 9000 | 9120 | 8906 | 8766 | 8742 | 8668 | 8488 | 8265 | 7977 | 7630 | 7304 | 6987 | 6721 | 6405
Gen Profile (90) | 6081 | 5879 | 5745 | 5645 | 5566 | 5492 | 5437 | 5410 | 5394 | 5426 | 5465 | 5573 | 5643 | 5832 | 6002 | 6211 | 6320 | 6365 | 6384 | 6445 | 6496 | 6644 | 6835 | 6994 | 7187 | 7383 | 7564 | 7749 | 7956 | 8142 | 8349 | 8556 | 8768 | 8878 | 9000 | 9100 | 8906 | 8766 | 8742 | 8668 | 8488 | 8265 | 7977 | 7630 | 7304 | 6987 | 6721 | 6405
50 POE Demand + UM(95) | 6131 | 5929 | 5795 | 5695 | 5616 | 5542 | 5487 | 5460 | 5444 | 5476 | 5515 | 5623 | 5703 | 5902 | 6082 | 6301 | 6420 | 6475 | 6504 | 6575 | 6636 | 6794 | 6995 | 7164 | 7367 | 7573 | 7764 | 7959 | 8176 | 8372 | 8589 | 8806 | 9028 | 9148 | 9265 | 9269 | 9206 | 9076 | 9062 | 8998 | 8828 | 8615 | 8337 | 7930 | 7574 | 7237 | 6921 | 6545
Gen Profile (95) | 6131 | 5929 | 5795 | 5695 | 5616 | 5542 | 5487 | 5460 | 5444 | 5476 | 5515 | 5623 | 5703 | 5902 | 6082 | 6301 | 6420 | 6475 | 6504 | 6575 | 6636 | 6794 | 6995 | 7164 | 7367 | 7573 | 7764 | 7959 | 8176 | 8372 | 8589 | 8806 | 9028 | 9100 | 9100 | 9100 | 9100 | 9076 | 9062 | 8998 | 8828 | 8615 | 8337 | 7930 | 7574 | 7237 | 6921 | 6545
50 POE Demand + UM(99) | 6181 | 5979 | 5845 | 5745 | 5666 | 5592 | 5537 | 5510 | 5494 | 5526 | 5585 | 5713 | 5803 | 6012 | 6202 | 6431 | 6560 | 6625 | 6664 | 6745 | 6816 | 6984 | 7195 | 7374 | 7587 | 7803 | 8004 | 8209 | 8436 | 8642 | 8869 | 9096 | 9328 | 9458 | 9585 | 9599 | 9546 | 9426 | 9422 | 9368 | 9208 | 9005 | 8737 | 8330 | 8154 | 7787 | 7471 | 7105
Gen Profile (99) | 6181 | 5979 | 5845 | 5745 | 5666 | 5592 | 5537 | 5510 | 5494 | 5526 | 5585 | 5713 | 5803 | 6012 | 6202 | 6431 | 6560 | 6625 | 6664 | 6745 | 6816 | 6984 | 7195 | 7374 | 7587 | 7803 | 8004 | 8209 | 8436 | 8642 | 8869 | 9096 | 9100 | 9100 | 9100 | 9100 | 9100 | 9100 | 9100 | 9100 | 9100 | 9005 | 8737 | 8330 | 8154 | 7787 | 7471 | 7105
Deficit (90) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 20 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Deficit (95) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 48 | 165 | 169 | 106 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Deficit (99) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 228 | 358 | 485 | 499 | 446 | 326 | 322 | 268 | 108 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 8: Benefits of the Proposed Approach
Changing network
  more distributed generation
  Intra-regional contingencies have a more significant impact
A full network model provides
  flexibility in modelling various/unforeseen network configurations e.g. separation not occurring at regional boundary
  Information about network congestion at a nodal level hence provide information about impact of intra-regional contingencies
  Better forecast of demand and VRE based on locational weather patterns
  Better representation of WDR and DER

## Slide 9: Proof Of Concept
A PoC is being conducted to determine the feasibility and practicality of the proposed solution
This work includes four major workstreams. Three of the workstreams involve proving that
  reasonable forecasts of demand and variable renewable energy (VRE) can be produced at a nodal level;
  the proposed theory behind developing uncertainty margins at a nodal level can be applied practically; and
  an off-the-shelf software can be utilised (with some configuration) to develop a full network model that determines the appropriate generation dispatch profile and also suggests a RERT dispatch profile, if required.
The fourth work stream involves drafting the NER and related document changes that may be required to implement the new solution.
Based on 30 Dec 2019 event
  Extreme day - hot temperatures, high demand, bushfires
  Unplanned outage of 051 (Lower Tumut to Wagga 330 kV) line leading to
    reduction of ~1000 MW of reserve in Victoria
    Forecast LOR 2
    Activation of RERT

## Slide 10: Forecasting at nodal level
Load & VRE Forecast – Most Probable Forecast 50 POE
For VRE forecasts we already receive DUID level forecasts from AWEFS and ASEFS – these can be reused.
For load forecasts:
  The existing load forecasting methodology uses bespoke sub-region (area-level) load forecast models from the DFS.
  For the PoC these existing load forecast models are used with the forecasts disaggregated to the nodes using a load factor analysis based on the correlations of each node to the sub-regional load forecast.
  The intention in a full implementation is to have the ability to create load forecasts at the zonal-level as and when the load forecasting system is further developed. The initial thought is that the zonal-level will roughly correspond to micro-climate zones, based on discussion with other ISOs around pros/cons/accuracy/scalability/maintainability trade-offs.

## Slide 11: Accounting for uncertainty
Accounting for uncertainty: “Uncertainty Margin”
  An amount of MWs that represents expected forecast error given a confidence level, used to adjust the load and VRE forecasts and ensure sufficient supply to meet demand
  Understanding of forecasting errors at different forecast lead times and in different conditions (such as weather)
  Margins based on distribution of forecast errors
  Note that uncertainty margins should eventually incorporate the forced outage rates for dispatchable generators. The optimiser will take into account requirements to manage frequency via FCAS requirements (still to be confirmed).
How to determine the uncertainty margin? A few options:
  1. Empirically from historical forecast errors under different conditions
    Pros: computationally simple; Cons: subject to discontinuity and difficult to scale.
  2. Develop a model to predict forecast error given expected conditions
    Pros: dynamic, continuous values under varying conditions; Cons: large amount of computer processing power required to train models or will require substantial statistical modelling to find a suitable parametric model for how the distribution of forecast errors changes over time and with forecast weather conditions.
How to determine the confidence level? Work in progress
  x% confidence level means that we are x% confident that the forecast error will not exceed this value
  Do we select a 90%, 95%, 99% or some other confidence level?
  Ideas:
    Confidence level can be selected by performing a sensitivity analysis of case studies using different confidence levels
    Assessment of false-positives, true-positives, false-negatives and true-negatives
    Different confidence levels for different horizons or load/generator types
    Ultimately the approach to determining the confidence intervals should be tuned to be consistent with the reliability standard

## Slide 12: Accounting for uncertainty
Preliminary numbers for the PoC scenario (30/12/2019 14:30) showing the reliability margin for the load forecast under different confidence levels and different forecast horizons. These numbers WILL change as the modelling is refined.
Region | 4hrs ahead |  |  | 24hrs ahead |  |  | 7days ahead |  | 
Confidence level | 90% | 95% | 99% | 90% | 95% | 99% | 90% | 95% | 99%
QLD | 270MW | 370MW | 890MW | 300MW | 400MW | 930MW | 380MW | 620MW | 1130MW
NSW | 390MW | 590MW | 1100MW | 400MW | 600MW | 1140MW | 460MW | 790MW | 1770MW
VIC | 360MW | 550MW | 1120MW | 380MW | 570MW | 1160MW | 440MW | 750MW | 1810MW
SA | 110MW | 180MW | 400MW | 120MW | 200MW | 410MW | 150MW | 240MW | 540MW
TAS | 100MW | 160MW | 650MW | 140MW | 190MW | 660MW | 140MW | 210MW | 710MW

## Slide 13: The optimiser
The optimiser engine will determine the most economic generation profile that would meet the load (50 POE demand plus Uncertainty Margin) subject to n-1 security (transmission plus generation) constraints + frequency control constraints (TBD)
To prove that an off-the shelf software can be used to develop the network model and determine an appropriate generation dispatch profile
  Have reached out to some software vendors

## Slide 14: The optimiser – Progress to date
Have run some basic runs
  Results being examined
For finalised PoC
  Full ‘n-1’ secure system (using thermal, stability & system strength constraints)
  Load forecast plus uncertainty margin
  Multiple intervals

## Slide 15: Work still in progress

## Slide 16: WIP – LOR Levels
Rules require AEMO to determine and report on at least three “loss of load probability” levels at which AEMO will declare a corresponding LOR condition
No direct co-relation between current LOR levels and the new paradigm.
AEMO will work with stakeholders in the project’s design phase to determine the intervention level.
The following slide puts forward a proposal of determining the new LOR levels and corresponding runs

## Slide 17: WIP – LOR Levels
Current ST PASA |  | Proposed System | 
Current LOR Levels | Intervene in Market? | Proposed LOR levels | Intervene in Market?
LOR 3 – Cannot meet demand if we have a credible network contingency | Y | LOR RED – Cannot meet demand if we have a credible network contingency OR a trip of any generator in the NEM Demand = 50 POE demand plus Uncertainty Margin at x%1 confidence level | Y
LOR 2 – Cannot meet demand if we have a credible network contingency OR a trip of the largest generator (in that region) (FUM is also considered at this point) | Y |  | 
LOR 1 - Cannot meet demand if we have a credible network contingency OR a trip of the largest and the second largest generator (in that region) (FUM is also considered at this point) | N | LOR ORANGE – Cannot meet demand if we have a credible network contingency OR a trip of any generator in the NEM Demand = 50 POE demand plus Uncertainty Margin at y% confidence level (where y>x) | N
 |  | LOR YELLOW – Cannot meet demand if we have a credible network contingency OR a trip of any generator in the NEM Demand = 50 POE demand plus Uncertainty Margin at z% confidence level (where z>y>x) | N
1 x% is the AEMO intervention level

## Slide 18: WIP – LOR Levels
Example above would be
LOR RED for Interval 36
LOR ORANGE for Intervals 34,35 & 37
LOR YELLOW for Intervals 33, 38 - 41
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48
50 POE Demand + UM(90) | 6081 | 5879 | 5745 | 5645 | 5566 | 5492 | 5437 | 5410 | 5394 | 5426 | 5465 | 5573 | 5643 | 5832 | 6002 | 6211 | 6320 | 6365 | 6384 | 6445 | 6496 | 6644 | 6835 | 6994 | 7187 | 7383 | 7564 | 7749 | 7956 | 8142 | 8349 | 8556 | 8768 | 8878 | 9000 | 9120 | 8906 | 8766 | 8742 | 8668 | 8488 | 8265 | 7977 | 7630 | 7304 | 6987 | 6721 | 6405
Gen Profile (90) | 6081 | 5879 | 5745 | 5645 | 5566 | 5492 | 5437 | 5410 | 5394 | 5426 | 5465 | 5573 | 5643 | 5832 | 6002 | 6211 | 6320 | 6365 | 6384 | 6445 | 6496 | 6644 | 6835 | 6994 | 7187 | 7383 | 7564 | 7749 | 7956 | 8142 | 8349 | 8556 | 8768 | 8878 | 9000 | 9100 | 8906 | 8766 | 8742 | 8668 | 8488 | 8265 | 7977 | 7630 | 7304 | 6987 | 6721 | 6405
50 POE Demand + UM(95) | 6131 | 5929 | 5795 | 5695 | 5616 | 5542 | 5487 | 5460 | 5444 | 5476 | 5515 | 5623 | 5703 | 5902 | 6082 | 6301 | 6420 | 6475 | 6504 | 6575 | 6636 | 6794 | 6995 | 7164 | 7367 | 7573 | 7764 | 7959 | 8176 | 8372 | 8589 | 8806 | 9028 | 9148 | 9265 | 9269 | 9206 | 9076 | 9062 | 8998 | 8828 | 8615 | 8337 | 7930 | 7574 | 7237 | 6921 | 6545
Gen Profile (95) | 6131 | 5929 | 5795 | 5695 | 5616 | 5542 | 5487 | 5460 | 5444 | 5476 | 5515 | 5623 | 5703 | 5902 | 6082 | 6301 | 6420 | 6475 | 6504 | 6575 | 6636 | 6794 | 6995 | 7164 | 7367 | 7573 | 7764 | 7959 | 8176 | 8372 | 8589 | 8806 | 9028 | 9100 | 9100 | 9100 | 9100 | 9076 | 9062 | 8998 | 8828 | 8615 | 8337 | 7930 | 7574 | 7237 | 6921 | 6545
50 POE Demand + UM(99) | 6181 | 5979 | 5845 | 5745 | 5666 | 5592 | 5537 | 5510 | 5494 | 5526 | 5585 | 5713 | 5803 | 6012 | 6202 | 6431 | 6560 | 6625 | 6664 | 6745 | 6816 | 6984 | 7195 | 7374 | 7587 | 7803 | 8004 | 8209 | 8436 | 8642 | 8869 | 9096 | 9328 | 9458 | 9585 | 9599 | 9546 | 9426 | 9422 | 9368 | 9208 | 9005 | 8737 | 8330 | 8154 | 7787 | 7471 | 7105
Gen Profile (99) | 6181 | 5979 | 5845 | 5745 | 5666 | 5592 | 5537 | 5510 | 5494 | 5526 | 5585 | 5713 | 5803 | 6012 | 6202 | 6431 | 6560 | 6625 | 6664 | 6745 | 6816 | 6984 | 7195 | 7374 | 7587 | 7803 | 8004 | 8209 | 8436 | 8642 | 8869 | 9096 | 9100 | 9100 | 9100 | 9100 | 9100 | 9100 | 9100 | 9100 | 9100 | 9005 | 8737 | 8330 | 8154 | 7787 | 7471 | 7105
Deficit (90) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 20 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Deficit (95) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 48 | 165 | 169 | 106 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Deficit (99) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 228 | 358 | 485 | 499 | 446 | 326 | 322 | 268 | 108 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 19: WIP - Run types
To determine the LOR levels described previously we will require the following runs
  ‘Base’ run
    load forecast + uncertainty margin at x% confidence level
    Include network and generator contingencies to ensure n-1 secure
    Create a dispatch profile and show deficits at a nodal level
    If any deficits are determined, then create a RERT schedule in case intervention is required
    AEMO will intervene and commit RERT based on this run only
  Other runs at a higher confidence levels
    This would be used for situational awareness only – provide a warning to market
  ‘Scenario’ run
    Other runs used for AEMO’s situational awareness only.
    E.g. n-2 security run, extreme weather scenario

## Slide 20: WIP – frequency of runs
Requirements for notification of reliability issues vary according to time horizons
The following could be considered as an option
Note:
No analysis has been done yet on how long each run takes to run
Would have to look at continuity of results between runs
Start Interval | End Interval | Interval length | Frequency
Now | End of current pre-dispatch period | 30 minutes | 30 minutes
End of current pre-dispatch period | 4 days | 30 minutes | 1 hour
4 days | 7 days | 30 minutes | 2-4 hours

## Slide 21: WIP - Display
Looking at heat maps as potential method of displaying areas of concern
Example on right
  Optimiser results for 1430 hrs 30 Dec 2019
  Based on 24 hour-ahead forecasts @99% Confidence level
  Supply deficits shown by circle colour and size
  Large 1100 MW deficit at Melbourne (VIC) (red dots)
  Minor deficits at Bannerton (VIC), Blackwater (QLD) and Brisbane (QLD) (green dots)

## Slide 22: Other areas still be considered
How energy limited plant and energy storage devices are modelled
How/if generator forced outage rates are used in determining uncertainty margins
  Currently we think the outages rates can be incorporated into the uncertainty margin via a convolution method
How to provide information about network outages that are restricting the network flow and contributing to deficits
How/if FCAS or spinning reserve is considered
How inertia and system strength issues will be identified
How DER is modelled

## Slide 23: Next steps
Deliverable/Milestone | Detail | Indicative Date
Finalise PoC | Finalise PoC , showcase results and seek senior management approval to continue | Jan 2021
Commence Detailed Design phase | Commence development of detailed design (pending budget approval) | Feb 2021
Stakeholder Consultation/s | Showcase PoC results and consult with Industry | Feb 2021 and beyond
Rule change proposal | Develop and submit Rule Change proposal | Q1 2021
Commence Implementation Phase | Commence implementation of new design (pending budget approval) | Q4 2021
Proposed Completion | Proposed Go Live | Q3 2022

## Slide 24: Communication with AEMO
Any communication including comments/questions can be sent to STPASAReplacement@aemo.com.au