## Slide 1: Joint Dispatch/Systems Focus Group
22 October 2018
AEMO Office, Level 10, 10 Eagle St, Brisbane
This slide pack was developed for the Joint Dispatch/Systems Focus Group meeting. This version of the slides has been annotated with notes from the meeting. These additional notes are either in blue text or on new slides that have a yellow background.

## Slide 2: Agenda
NO |  | Time | AGENDA ITEM | Responsible
Preliminary Matters |  |  |  | 
1 | 10:00am – 10:10am | 10:00am – 10:10am | Welcome, introduction and apologies | Michael Sanders (AEMO)
2 | 10:10am – 10:20am | 10:10am – 10:20am | Actions from previous meeting | Michael Sanders (AEMO)
Matters for Noting |  |  |  | 
3 | 10:20am – 10:35am | 10:20am – 10:35am | Extending and expanding 5-minute pre-dispatch | Hamish McNeish (AEMO)
4 | 10:35am – 10:45am | 10:35am – 10:45am | Use of 5-minute data in 30-minute processes | Michael Sanders (AEMO)
Matters for Discussion |  |  |  | 
5 |  |  | Transition to 5 minute bidding | 
5a | 10:45am – 12:00pm | 10:45am – 12:00pm | AEMO’s plan for transition | Pierre Fromager, Michael Sanders & Hamish McNeish (AEMO)
 | 12:00pm – 12:30pm | 12:00pm – 12:30pm | LUNCH | 
5b | 12:30pm to 1:00pm | 12:30pm to 1:00pm | When are participants planning to transition? | Feedback from participants
6 | 1:00pm to 1:40pm | 1:00pm to 1:40pm | Dispatch instruction timing | Michael Sanders (AEMO)
7 | 1:40pm – 1:50pm | 1:40pm – 1:50pm | “Zero” fixed load | Michael Sanders (AEMO)
Other business |  |  |  | 
8 | 1:50pm – 2:00pm | 1:50pm – 2:00pm | General questions | Michael Sanders & Hamish McNeish (AEMO)
9 | 2:00pm - 2:05pm | 2:00pm - 2:05pm | Next steps | Michael Sanders & Hamish McNeish (AEMO)

## Slide 3: Attendees
Name | Company
Boris Basich | AGL
Marc L’Estrange | AGL
Chris Pratt | Alinta
Zahir Ally | Alinta
Benn Blumenthal | CS Energy
Brian McKerr | CS Energy
Henry Gorniak | CS Energy
Jeramy Mendoza | EnergyAustralia
Sharleen Flanagan | ERM Power
Jarrah van Rijswijk | Hydro Tas
Stephanie Easton | Infigen
Victor Sanchez | Infigen
Chris Tetzke | Intergen
Name | Company
Wayne Baldwin | Intergen
Methsiri Aratchige | Origin Energy
Olivia Fleming | Origin Energy
Hugh Macfarlane | Snowy
Adam Branson | Stanwell
Adam Neilson | Stanwell
Oliver Jessup | Stanwell
Emily Brodie | AEMO
Tom Butterworth | AEMO
Pierre Fromager | AEMO
Hamish McNeish | AEMO
Michael Sanders | AEMO

## Slide 4: Actions from previous meeting
Michael Sanders

## Slide 5: Response to actions from 14th August Dispatch Focus Group (1)
 | Topic | AEMO action | Response
1 | Sparse bidding formats | Refer web interface speed and accuracy issues to the SWG for consideration in that forum | The web interface functionality will be discussed in a SWG focus group planned for November. End users are interested in being involved in design sessions. ACTION: AEMO to set focus group meeting and agenda, and communicate to participants.
2 | Transitional arrangements | Refer transitional arrangements (ability to submit 5 minute and 30 minute bids etc) to the SWG for detailed investigation in that forum, or potentially via a joint SWG/PWG focus group. | Joint focus group planned for Monday 22 October in Brisbane
3 | Other issues | Investigate the computational limitations on extending and expanding 5MPD. Report back to the Dispatch Focus Group and PWG. | Investigating computation limitations for extending 5MPD, results likely in early November 2018. Will investigate the computation limitations for expanding 5MPD to include multiple scenarios in Q1, 2019. For reference, the current 5MPD is published on average 77 seconds after the start of the first 5 minutes. The solve takes on average 36 seconds for 6 five minute periods.

## Slide 6: Response to actions from 14th August Dispatch Focus Group (2)
 | Topic | AEMO action | Response
4 | Other issues | Investigate the lag between the start of the trading interval and the receipt of dispatch instructions. Report back to the Dispatch Focus Group, PWG and SWG. | The causes and consequences of this issue are being investigated by AEMO’s Electricity Market Monitoring team. Under normal circumstances the dispatch solves takes 8 seconds on average. Distribution is normally completed 22 seconds after the start of a 5 minute period. When multiple solutions are required (such as with interventions) the solve times will be longer, which will delay distribution.
5 | Other issues | Investigate risks and benefits associated with the alignment of the electricity trading day with either the gas trading day or the calendar day (i.e. midnight). Report back to the Dispatch Focus Group and PWG. | Considered unnecessary for 5MS to proceed Would require a Rule change via AEMC process Aligning NEM day to gas day would exacerbate existing issue in NEM relating to transfer of ownership & new owner’s ability to enter/change bids Aligning NEM day to midnight (to relieve the above issue) would increase disparity between NEM and Gas trading days

## Slide 7: Response to actions from 14th August Dispatch Focus Group - Discussion
There was appetite from several participants to investigate aligning the electricity day with the calendar day. This would be driven by participants outside of the 5MS project.
Alignment would require a rule change. Guidance for making a rule change request can be found at: https://www.aemc.gov.au/our-work/changing-energy-rules-unique-process/making-rule-change-request/tips-making-rule-change

## Slide 8: Extending and expanding 5-minute pre-dispatch
Hamish McNeish

## Slide 9: Current situation
Current situation for 5-minute pre-dispatch
  Is not mandated in the Rules
  Covers 12 x 5-minute intervals (60 minutes)
  Has no price sensitivities
  Is computationally intense
  Calculations are sequential with results of each interval being used as inputs to the next interval

## Slide 10: Dispatch and Pre-dispatch timings (avg.)
Notes
The process completion and publication times are average times based on normal market conditions. Under conditions such as intervention where multiple solutions are required, these times will be longer.
These times are sourced from AEMO’s performance monitoring systems. Actual times at participants’ sites will be dependent on the local infrastructure and configuration.
In the case of the 30-minute Pre-dispatch, there is a larger variation of times around the average due to the variable length in time of the Pre-dispatch schedule.
 | Dispatch | 5-minute Pre-dispatch | 30-minute Pre-dispatch
Period (cycle) | 5 min | 5 min | 30 min
Horizon | 5 min | 60 min | 16 to 40 hours 3
Resolution | 5 min | 5 min | 30 min
Process start | t-67 sec | t-67 sec | t+0 sec
SCADA Snapshot | t-3 sec | t-3 sec | ~t+10 sec
Process complete1 | t+8 sec | t+36 sec | t+140 sec
Solution published | t+17 sec | t+48 sec | t+155 sec
Data loaded to participants’ database 2 | t+22 sec | t+77 sec | t+174 sec

## Slide 11: Possible Options
The P5 timings need to be investigated further by AEMO, including timings around producing price sensitivities.
The current P5 implementation requires each interval to be solved sequentially limiting what can be implemented.
Option 1: Extend the current 5-mn Pre-dispatch
  Needs to be produced every 5 minutes
  1 hour (12 periods) takes around 1.3 minutes to produce
  6 hour (72 periods) is expected to take between 6 and 10 minutes to produce
  3 hours (36 periods) is expected to take between 3 and 5 minutes to produce
  It’s likely we can extend to 3 hours (without sensitivities)
Option 2: Additional 6 hour 5-mn Pre-dispatch schedule
  6 hour (72 periods) is expected to take between 6 and 10 minutes to produce
  The final solution would diverge from the 1 hour runs that occurred in the interim
  The schedule is expected to be published wither every 10 or 15 minutes
Option 3: Additional 24 hour 5-mn Pre-dispatch schedule
  24 hour (288 periods) is expected to take between 24 to 40 minutes to produce
  The final solution would diverge from the 1 hour runs that occurred in the interim
  The schedule is expected be be published every 60 minutes

## Slide 12: Possible Options
AEMO’s position:
  The current 1 hour, 5-mn Pre-dispatch schedule could be extended but needs to continue to be published every 5 minutes.
  AEMO can investigate the possibility of additional 5-min Pre-dispatch schedules based on participants’ feedback and preference.

## Slide 13: Extending and expanding 5-minute pre-dispatch - NOTES
Planning data has a diminishing value as time extends out. Participants indicated that it is more important to get accurate information more often. For example, period-by-period solution: calculate period 1, publish results, calculate period 2, publish that, etc. Noting that time might be lost in publishing.
  ACTION: AEMO to investigate and communicate how long it takes to publish data
Participants noted that will need to look ahead as much as possible for resource planning, especially for pricing. Price sensitivities are critical, in the first hour especially. Traders want visibility on bidding activity and price visibility further out.
There was discussion about inclusion of fast-start inflexibility profile in P5. NER states that these should not be used in PD.
  ACTION: AEMO to investigate inclusion of fast-start inflexibility profiles in P5, potentially as part of the drafting amendments rule change request (targeted for January 2019).
P5 does take intervention into consideration (considerably slowing calculations). Note that if multiple regions are affected, the calculation time is no worse. E.g. Qld and SA are affected, calculations do not solve for Qld then SA; they do both.

## Slide 14: Use of 5-minute data in 30-minute processes
Michael Sanders

## Slide 15: Use of 5-minute data in ST PASA
Current default position:
  Use the 5-minute bid that has the lowest availability within each 30-minute period
This is consistent with the purpose of PASA i.e. to identify any projected shortfalls in supply.

## Slide 16: Use of 5-minute data in 30-minute pre-dispatch
Current default position:
  Use the last (6th) 5-minute bid within each 30-minute period
Dispatch Focus Group raised concerns that this might lead to misleading 6th-interval bidding
AEMO’s view is that:
  We need to choose a fixed 5-minute interval within the 30-minute period (no randomising, no averaging)
  NER 3.8.22A mitigates the risk (offers, bids and rebids must not be false or misleading)
  The focus will shift more to 5-minute pre-dispatch with 5-minute settlement

## Slide 17: Use of 5 minute data in 30 minute processes - NOTES
ST PASA
AEMO Operations is investigating the operational implications of using the 5-minute bid with the lowest availability in each 30-minute period
Participants also expressed interest in:
  ST PASA using an average availability over the 30-minute period; and
  ST PASA having a 5-minute resolution. The Rules require publication of ST PASA with a 30-minute resolution, so providing an ST PASA with 5-minute resolution would require a Rule change, or an additional process.
AEMO’s view is that the case for 5-minute resolution ST PASA has yet to be established. AEMO will continue with 30-minute resolution ST PASA as required by the NER.

## Slide 18: Use of 5 minute data in 30 minute processes - NOTES cont’d
Pre-Dispatch (PD)
Participants continued to express concerns that using the last 5-minute bid within each 30-minute period would invite gaming
AEMO believes that any gaming concerns will be mitigated by:
  the bidding in good faith rules (NER 3.8.22A); and
  an extension of the time horizon for 5-minute pre-dispatch (P5)
Participants also expressed interest in replacing PD with P5
There are doubts about the feasibility of solution times and data volumes if P5 is extended to the PD timeframe, even before adding sensitivities.

## Slide 19: Transition to 5-minute bidding - AEMO’s plan for transition
Michael Sanders & Hamish McNeish

## Slide 20: Allow 5-mn bids before commencement date
Although the Rules state that the changes will take effect on 1 July 2021, AEMO has identified that it would be prudent to introduce some of the changes before commencement. Some participants identified, in the Dispatch Focus Group, that this could impact the market and give unfair advantage to early adopters.
Options include:
Reject Unable to accept 5-mn bids until commencement.
Accept 5-mn bids 3 months before commencement, allowing enough time for AEMO and participants to evaluate the impact of system changes, keeping old processes for security. Use these bids directly in the dispatch process.
Accept 5-mn bids much earlier, say 6 to 12 months, or much later, say, 2-4 weeks before commencement. Participants were not supportive of this option
Accept 5-mn bids but convert them to 30-mn bids until commencement. This option was rejected by both AEMO and participants due to the complexity of conversion.

## Slide 21: Allow 5-mn bids before commencement date
AEMO’s position:
Accept 5-mn bids from 1 April 2021, 3 months before commencement.
Use these directly in the NEMDE i.e. don’t transform these into 30-mn bids.
For 5-mn bids prices will remain to be set for a trading day, with capacity/availability quantities provided for each trading interval (288 intervals).
From 1 April 2021:
  existing 30-mn bids for trading days from 1/4/2021 have been converted to 5-mn bids by AEMO (during the release)
  any received 30-mn bids are converted to 5-mn bids by AEMO’s systems
  dispatch, pre-dispatch, PASA, etc. will run off 5-mn data.
5-mn bids will be provided in JSON format; 30-mn bids remain in TXT format.
The web portal supports both 30-mn and 5-mn bids during transition.
From commencement, 30-mn bids will be rejected as invalid.

## Slide 22: Acceptance of 30-mn and 5-mn bids
The following table shows the acceptance/rejection of 30-mn and 5-mn bids.
The Transition Period starts from the release date of 1 April 2021
Commencement is 1 July 2021

## Slide 23: Allow 5-mn bids before commencement date
Note that DS and P5Min currently use 5-mn dispatch intervals, so no change needed; PD & ST PASA are in 30-mn intervals
Assuming an early release is accepted, should a trading date be set a few days after the release, where the new 5-mn bids will be accepted? This would allow all participants to bed down the changes before starting the new bidding regime. Once the release occurs, AEMO will start accepting 5-minute bids.
  * For example, if the software release is on 1 April, 5-mn bids might be accepted for 15 April onwards.
Should 5-mn bid changes roll into schedules e.g. ST PASA, P5Min (if 24 hour), before dispatch. A worthwhile benefit is this also allows a few days to roll out system changes e.g. do PASA, then pre-dispatch, finally dispatch over a few days. Participants supported modular release timing. ACTION: AEMO to consult on software release approach.
Discussion

## Slide 24: Conversion between 30 and 5-mn bids
Assuming that 30-mn bids are accepted for a period where 5-mn bids are in effect, a recognised process is required for conversion.
The Amendment Rule below addresses this.
    National Electricity Amendment (Five minute settlement) Rule 2017 No. 15, 11.103.7: “Any dispatch offer or dispatch bid submitted pursuant to old clause 3.8.9 [“Default offers and bids”] for a trading interval prior to the commencement date will, from the commencement date, be deemed to be 6 equal dispatch offers or dispatch bids submitted in respect of the 6 consecutive trading intervals within the relevant 30-minute period until such time as that dispatch offer or dispatch bid is resubmitted under new clause 3.8.9.”
AEMO proposes to also apply this conversion process during the trial period i.e. a 30-mn bid is converted to six 5-mn bids of the same prices and quantities as the 30-mn bid.
Participants accepted this approach.
This would also include the PASA 24-hour availability specified in the bid.

## Slide 25: Commencement 12-4 am
The 5MS Rule comes into effect on 1 July 2021 at 12 am.
The June 30 trading-day includes the intervals from 12 am to 4 am.
  Specific functionality to convert 30-mn to 5-mn may be required, depending on the policy requirement for when five-minute bidding comes into effect.
AEMO’s position:
  Accept 5-mn bids from 1 April 2021 and convert 30-mn bids at this time. Participants accepted this approach.
  From 00:00 hrs on 1 July 2021, reject any received 30-mn bids as invalid.

## Slide 26: 30-mn bids after Commencement
The Rules mandate that these changes take effect on 1 July 2021. Hence, no 30-mn bids should be accepted after this time.
AEMO’s position: Reject 30-mn bids for Trading Days after commencement from 00:00 hrs 1 July 2021.
Discussion:
See the Conversion section for default and rolling bids.

## Slide 27: Accepting bids - NOTES
Participants would prefer to continue conversion beyond commencement, noting that some small participants may not be ready for 5-minute bidding by commencement.
AEMO’s view is that the 5MS Rule requires participants to submit 5-minute bids from commencement.
ACTION: AEMO to monitor participant bidding as part of readiness for 5MS

## Slide 28: Submission of FTP, Web and API bids
Bid submission will transition from TXT based to a JSON format
  5-mn bids can only be submitted in the JSON format
  30-mn bids can only be supported in the TXT format
  The web UI will provide screens to submit either (during the trial period)
Current
  Participants currently submit text files through FTP.
Proposed
  AEMO has identified an opportunity to improve this process by using a more flexible, accurate, text-based format for the submissions, called JSON (JavaScript Online Notation). These would be submitted via
    FTP (same process as today),
    Web UI (enhanced interface)
    APIs or
    by submission of a JSON file through the Web portal.
  AEMO is also considering support uploading a CSV format via the web portal only, to support low frequency bidding where systems such as Excel are used to create bidding files.
  Participants accepted this approach.

## Slide 29: Submission of FTP, Web and API bids
AEMO have proposed that only JSON format bids will be accepted after commencement. This section focusses on the pre-commencement period.
AEMO’s position: Accept JSON format bids in Production three months before commencement (i.e. from 1 Apr 2021). Allow all three methods: APIs, FTP, and Web submissions.
Discussion:
How early before commencement should JSON format bids be accepted?
  Note that JSON format bids cannot be used for 30-mn bids. Participants accepted this approach.
Is there a priority for one of the methods before the others?
  For example, is it worth just releasing FTP before APIs or Web portal? Participants were strongly supportive of the API submission method.
Allow JSON format bids before commencement

## Slide 30: Submission of FTP, Web and API bids
AEMO’s position: Discontinue use of TXT files at commencement. Participants were supportive of TXT file submission being continued beyond commencement to support small participants.
Disallow TXT files
after commencement

## Slide 31: Submission of bids - NOTES
Participants asked if an API simulator environment provided to participants was possible.
ACTION: AEMO will provide the API Swagger files. From this participants can mimic the API’s.
Participants indicated the priority for the sandbox was:
  Web API interface – as this presents new technology/interfaces
  FTP interface
  Bidding data model
  Settlement data model – SETGENDATA report/table was also raised

## Slide 32: Reporting – Pre-dispatch, ST PASA
AEMO does not expect changes to reporting for dispatch, pre-dispatch or PASA. Apart from options for 5-mn Pre-dispatch (increasing length/price sensitivities etc.).
Discussion:
For an early release, bid reporting will need to support 5-mn bids. If there are changes to reporting granularity, can these be introduced early? AEMO will introduce 5-minute reporting in transition period.
Is there specific 30-mn intervals reporting that needs to remain? AEMO will continue to report in intervals consistent with the NER.
Are there changes required to ST PASA or other pre-dispatch report formats? No

## Slide 33: Bid reporting
Submitted 5-mn and 30-mn bids will need to be reported
It will be important to be able to determine which bids were submitted and at what resolution.
AEMO’s position:
During the trial period there will be both 30-mn and 5-mn reports available. However the 30-mn reports will not include 5-mn bids.
From commencement, the 30-mn bids would no longer be changing, so the 30-mn bid reports would become historic.
Both the 30-mn and 5-mn submissions will be available as files (AEMO will convert and store API payloads as files), as bids are now.
Participants accepted approach.

## Slide 34: Transition to 5-minute bidding - when are participants planning to transition?
Feedback from participants

## Slide 35: Participants’ plans
AEMO Timeline for 5-mn bidding
  Pre-production by Nov 2020 (dependent on early release date)
  Production by 1 Apr 2021
  Commencement 1 Jul 2021
How suitable are these dates considering market risks and participants' systems delivery?

## Slide 36: Transition to 5-minute bidding - when are participants planning to transition? - NOTES
Participants noted a need for file and API specifications.
  ACTION: AEMO to provide API specifications in line with SWG schedule.
Participants repeated the importance of an early sandbox environment. AEMO have committed to providing this.
  ACTION: AEMO to provide a sandbox timeline and scope
Real pricing and metering data would be preferable but not essential
  Pricing in the sandbox will be based on submitted offers and other data inputs to pricing may be static (such as constraints).
  Meter data is likely to be static.

## Slide 37: Dispatch instruction timing
Michael Sanders

## Slide 38: Current dispatch instruction timing
    Approximate dispatch instruction timings:
    Solution and publishing times will be longer if intervention, fast start +/or non-physical loss runs are required
Collect inputs and wait for SCADA read
T- 67s
SCADA snapshot
T-3 s
Data published to participants
T+17 s
NEM dispatch solution complete
T+8 s
Data to participant database
T+22

## Slide 39: Dispatch instruction timing issues
Time spent processing and publishing the dispatch solution
  Can this be reduced?
Time at which the dispatch solution is triggered
  Does moving the trigger earlier in the previous interval solve the problem or introduce new problems?
What are the costs of this issue to participants?

## Slide 40: Dispatch instruction timing - NOTES
AEMO is addressing this issue separately from the 5-minute settlement system changes
Participants noted existing compliance issues with SCADA InitialMW being measured before the end of the dispatch interval
AEMO is still investigating the potential for, and consequences of, timing changes
  ACTION: Participants to provide cost impacts of dispatch instruction timing under 5MS.

## Slide 41: “Zero” fixed load
Michael Sanders

## Slide 42: “0” fixed load
Current use
NER 3.8.19 lets participants submit a fixed load e.g. for testing
AEMO’s bidding systems currently interpret a “0” fixed load as a null fixed load i.e. there is no fixed load
  Some participants submit Fixed = 0, when what they mean is no fixed load
Proposed use
AEMO is proposing a move to an unambiguous interpretation where “0” means “0”
  The software has been developed and tested
  The shift to 5-minute bidding might be a good time to publicise and make the change

## Slide 43: “Zero” fixed load - NOTES
The system change has been developed and tested but not implemented
AEMO intends to introduce the change in parallel with the cutover to 5-minute settlement, due to the increased interaction with participants at that time
Some participants questioned the need for change. Others supported it. AEMO intends to proceed with it.

## Slide 44: General questions
Michael Sanders & Hamish McNeish

## Slide 45: Next steps
Michael Sanders & Hamish McNeish

## Slide 46: Next steps
SWG #3 – 30 October, AEMO offices
Joint dispatch/systems focus group – Bidding web user interface (mid-late November, Melbourne). Candidates are those who rely on the bidding web interface to view and submit and retrieve their bids.
Bids/Offers document:
  Marked-up version for comment: early-mid February 2019
  Final version published: late March 2019

## Slide 47: Next steps - NOTES
ACTION: AEMO to consider aligning the November dispatch/systems focus group with the AS-TAG or other FCAS working group

## Slide 48: Summary of actions
Item | Action | Responsible | Due date
2 | AEMO to set focus group meeting and agenda, and communicate to participants. | AEMO | 31 October 2018
3 | AEMO to investigate and communicate how long it takes to publish data | AEMO | TBC
3 | AEMO to investigate inclusion of fast-start inflexibility profiles in P5, potentially as part of the drafting amendments rule change request (targeted for January 2019). | AEMO | 30 November 2018
5a | AEMO to consult on software release approach. | AEMO | November 2018
5a | AEMO to monitor participant bidding as part of readiness for 5MS | AEMO | November 2020
5a | AEMO will provide the API Swagger files. | AEMO | TBC
5b | AEMO to provide API specifications in line with SWG schedule. | AEMO | February 2019
5b | AEMO to provide a sandbox timeline and scope | AEMO | December 2018
6 | Participants to provide cost impacts of dispatch instruction timing under 5MS. | Participants | 31 December 2018
9 | AEMO to consider aligning the November dispatch/systems focus group with the AS-TAG or other FCAS working group | AEMO | 31 October 2018