## Slide 1: GWCF report DWGM Enhancement WG
10 Dec 2020

## Slide 2: DWGM Enhancement WG Scope
Capacity
System capability modelling
Zonal capacity
Ancillary and Uplift
Ancillary payment changes
Uplift payment changes
Other changes
Tie breaking using CC
Scaling of CC for maintenance
Zone definition
Auctions
Products
Auctions
DTS SP allocations
CC Transfers
CC Listings
Other CC related
Procedure changes
General

## Slide 3: Changes to Market Design GWCF Sep 2020
To avoid repetition, will only go over changes since last GWCF
Changes to the Market Design Presentation
  Changes in orange text
The link block arrow jumps to the next change
Next Update

## Slide 4: Capacity certificates (CC) recap
All AMDQ replaced by CC and retired 31 Dec 2022
Scheduling will be to actual system capacity
  CC for tie breaking only
  Do not need to hold CC to be scheduled
CC will be:
  Issued for a calendar month
  Auctioned in multiple tranches twice a year over 3 years (ie 6 tranches)
    In some circumstances allocated by DTS SP
    Transitional auctions prior to first scheduled auction allowed
    Payment before CC issued to auction winners
  Based on system capability modelling that is refined over time
CC may be transferred from one MP to another MP using market systems
  Listing service for buyers and sellers of CC

## Slide 5: Capacity

## Slide 6: System capability modelling
On similar 1:20 peak day forecast basis as VGPR, and using same data
  Only one year of monthly data, but that will be extrapolated to 3 year outlook
  Completed by March each year, and updated post winter if relevant
Only includes committed projects for DTS or connected facilities
  As per VGPR requirements to provide information
  Details of upcoming projects included in VGPR and auction notices
  Take a conservative view of completion for projects that increase capacity
Excludes any planned maintenance
  Execution of maintenance could be affected by many factors
Basis for determination of the quantity of monthly auction products
  Published after completion of modelling
  Showing quantities to be allocated by auction and by DTS SP
  Qty can be adjusted if capacity changes before fully auctioned

## Slide 7: Capacity Certificate Zones
CC will be for entry or exit in a zone
  Entry Zone for system injection points
  Exit Zone for system withdrawal points
Zone will be as large as possible to maximise flexibility of use
AEMO proposes zones and consults with MP
  Min 4 weeks for consultation
  Consultation supported by modelling
    Including future enhancements where known
New connections may require changes to zones
  Consultation will include proposals to re-allocate CC in current zone

## Slide 8: Zonal capacity
Zonal capacity is determined from:
  system capability modelling (pipeline capacity)
  information provided by connected facilities (system point capacity)
In general, the zonal capacity is the minimum of pipeline capacity and total system point capacity
  Min ({Total pipeline capacity in zone}, {Total system point capacity in zone})
  Ignoring “back off effect” of multiple pipelines
    Flows on one pipeline may reduce capacity on another
    MP bidding behaviour will preference system points (ie price based)
      operational schedule constraints will manage back off effects
  Awaiting feedback from Nov WG on some more detailed options dealing with
    Exit capacity on SWP depending on GPG demand assumptions
    Entry capacity to be based on assumptions of likely flows from hub or maximum flows
Next Update

## Slide 9: Auction

## Slide 10: Auction of CC
Capacity will be auctioned:
in blocks of one calendar month (auction product)
for three years ahead (auction period)
2 months before earliest month being auctioned
  Auction Notice issued 20 business days before auction
    Includes qty, known maintenance, enhancements etc
at six monthly intervals
according to % of current zonal capacity to be released in each tranche (capacity release schedule)
Procedure will reflect as percentage of remaining capacity
  Allows auction to reflect capacity changes and unsold capacity in previous auctions
Tranche | Months | Tranche % | Cumul. %
1 | 1 -6 | 20% | 100%
2 | 7 -12 | 20% | 80%
3 | 13 – 18 | 15% | 60%
4 | 19 - 24 | 15% | 45%
5 | 25 – 30 | 15% | 30%
6 | 31 - 36 | 15% | 15%
Capacity Release Schedule

## Slide 11: Progressive auction #1
First auction in Nov 2022
System capability modelling updated after post winter review
Auction period Jan 23 – Dec 25
Capacity release schedule as shown

## Slide 12: Progressive auction #2
Second auction in May 2023
System capability modelling Mar 2023
Auction period Jul 23 – Jun 26
Capacity release schedule as shown

## Slide 13: Progressive auction #3
Third auction in May 2023 for Auction period Jan 24 – Dec 26
System capability modelling Oct 2023 – capacity increase from 150 to 200 TJ from Jan 2024
  Auction to cumulative percentage for each tranche less previously sold
    Tranche 1 (Jan 24 > Jun 24) – sell 100% of 200 less previously sold 80% of 150 = 80TJ
    Tranche 2 (Jul 24 > Dec 24) – sell 80% of 200 less previously sold 60% of 150 = 70TJ etc

## Slide 14: Progressive auctions 4 - 6
Jul 25 > Dec 26 fully auctioned through tranches
Blue shading unsold with rolling auctions

## Slide 15: Transitional auctions
Sold in two equal transitional auctions prior to Auction #1
Allows price discovery before Auction #1

## Slide 16: Auction general
10 bid steps per zone (GJ and $N.nnnn)
Linked bids will be possible:
  Where one CC without the another is not relevant to MP
    5,000 GJ of Gippsland Entry CC and Northern Exit CC for Jan 2023
  Over a period
    10,000 GJ of Culcairn Entry CC for Jan 2023 to Dec 2025
  Both multiple CC and periods possible
Auction system open for bids until 5pm AEST on day prior to processing
  Auction will run no later than 5pm AEST on day of processing
    Allows for resolution of system issues
  Report will be published
    Private report to MP on their position
    Public report on clearing prices and price sensitivities
      WG still considering options to publish de-identified bid stacks

## Slide 17: Auction general
Auction tie breaking must be random selection
  If 2 bids at same price, and cannot both be met, either
    1 randomly selected for partial quantity OR
    1 randomly selected to full quantity and other for remaining balance
Auction clearing price set for each zone at lowest successful bid price
  Zero dollars if auction capacity not cleared
Auction fee is payable on successful bids
Settlement via payment before CC are allocated to MP
  Not in DWGM prudential and settlement
  If CC not allocated due to non payment, included in next available auction
    Noting CC are not mandatory for bidding
  Payment for auctions via Austraclear 5 business days after auction
Next
Update

## Slide 18: CC Related

## Slide 19: DTS SP Allocation / CC Listing
Allocation of CC by DTS SP
If an expansion or extension of DTS is
  Not included in DTS SP capital base; AND
  AER has determined the portion of the additional capacity that is not approved CAPEX
DTS SP may direct AEMO to allocate the capacity to an MP
  MP must request allocation
CC listing service
Market systems will allow listing of:
  Offer to treat to buy CC
  Offer to treat to sell CC
No trading or settlement on market systems
  Any bilateral trades can be registered for transfer

## Slide 20: Transfer CC between MP
MP may transfer CC between themselves to reflect bilateral trading
  No market settlement of this trade
Covers whole auction product (block of one calendar month for a zone)
New market system for buyer to lodge and seller to confirm proposed transfer
  Must be an active MP to access system
  Transfer pending from lodgement until confirmation
  Confirmation must be by 12 midnight AEST on day of lodgement
    Unconfirmed transfers cancelled
  Lodgement & confirmation no later than 3 days before day of first gas day of auction product
    12 midnight AEST on 28 Sep for auction product for October
    Allows use of product for 2 day ahead provisional schedules
  AEMO & WG considering balance of month transfer
    No compelling case for them, so not part of design at this stage
Next
Update

## Slide 21: Ancillary Payments & Uplift Charges

## Slide 22: Ancillary payments (AP)
NGR removes requirement that AP not payable where supporting AMDQ
  Removes Injection hedge and Agency injection hedge nominations
WG supported removing Negative AP when previously scheduled bids are de-scheduled
  Bid steps at bid step prices at or near marginal prices may be scheduled and then de-scheduled in subsequent schedules.
  The PS and OS will match in these instances.
Principles in AP Procedure and formulae updated accordingly
AEMO identified that negative AP arise through MSIQ/MSWQ formulae, and will be replacing MSIQ/MSWQ with the Effective Pricing Schedule (EPS)
  Consistent with ancillary payment rule NGR 239(1) AP arise from OS and PS differences
  MSIQ/MSWQ uses EPS in many instances anyway
  Reduces complexity by removing a term from ancillary payment calculations
    Retaining MSIQ/MSWQ would mean significant additional complexity to exclude conditions that lead to negative AP
Next
Update

## Slide 23: Uplift payments (UP)
Rules introduce Uplift Payment Categories
  Must together recover AP total
  Previously specified congestion uplift only
    Removal of AMDQ means no congestion uplift as AMIQ exceedance cannot be determined
DTS Service Provider Uplift now only UP category mandated in rules
  Where DTS capacity falls below that specified in Service Envelope Agreement (SEA)
WG has not identified any additional UP categories leaving unchanged
  DTS SP liability cap exceedance uplift categories for event cap and annual cap exceedance
    Payment to DTS SP shown for transparency
  Surprise UP
  Common UP (incl unrecovered AEMO override)
DTS SP UP will only cover difference in AP resulting from constraint and AP that would have occurred if DTS operating at SEA capacity under same starting conditions
  AP that would have resulted while operating at SEA capacity recovered through other uplift
Next
Update

## Slide 24: Sequence of uplift payments
Total uplift payments are adjusted for successive positive and negative ancillary payments
  Know as “AP re-distribution” or “AP Flip Flop” algorithm
DTS SP uplift
  Cause of AP where SEA capacity not available
  Cap DTS SP Uplift GJ at AP GJ
  Determined at AP $ per GJ (positive only)
  Payment by DTS SP
Liability Caps
  Calculated as payment to DTS SP for exceedance
Surprise uplift
  Cause of AP above AP at SEA capacity
  Cap Surprise uplift GJ at AP GJ less DTS SP GJ
  determined at AP $ per GJ (positive or negative)
Common uplift
  AP less other UP categories
  Allocated based on MP withdrawals
Next
Update

## Slide 25: Other changes

## Slide 26: Use of CC for tie breaking
New NGR require that the Gas Scheduling Procedures must include details of the process to use CC for tie breaking
Currently MP must enter the percentage of AMDQ that is to be applied to each system injection point
The WG supported AEMO’s proposal that this would be automated
  An MP’s holding of CC in a zone will be allocated to
    Bid steps of any bids at all system point in a zone in price order
      Ascending for injection, descending for withdrawal
    To the extent of CC holdings for the gas day of the schedule
      Avail CC pro rated by bid step qty where price is tied and insufficient CC remain
    The scheduling process will give priority to those bid steps allocated CC
  MP will need to prioritise allocation of CC between system points through bid step prices
    $0.0000 allocated CC before $0.0001
Where multiple tied bid steps are fully supported by CC but cannot be fully scheduled
  tied bids will be pro-rated according to tied bid step quantities

## Slide 27: Scaling CC holdings
System capability modelling is excluding reduction of capacity due to maintenance
  Changing priorities mean maintenance may only be finalised at short notice
  Unplanned outages may also reduce capacity
Where maintenance reduces capacity, bid steps that exceed the available capacity and have CC will be scheduled to a greater extent than the proportion of CC holdings would indicate
  Such bids may not be made in good faith
The WG is currently considering options to equally scale CC holdings so that the total adjusted CC reflect the capacity that available in the schedule
  Maintains the proportionality of CC purchases

## Slide 28: Procedure changes
New procedures
  Capacity Certificates Auction Procedures
  Capacity Certificates Transfer Procedures
Procedures requiring review / changes
  Electronic Communication Procedures
  Gas Scheduling Procedures
  Ancillary Payment Procedures (and Ancillary Payment Functional Design)
  Uplift Payment Procedures (and Uplift Payment Functional Design)
  Accreditation Procedures
  Connection Approval Procedures
  Maintenance Planning Procedure
Retired Procedures
  AMDQ Procedures
  Injection Tie Breaking right functional design

## Slide 29: What next

## Slide 30: Next Steps
Finalise outstanding market design issues Q3/Q4 2020
  Market design to GWCF in Dec 2020 with GWCF WG report
AEMO drafts new and changed procedures Q4 2020
  Exposure drafts to DWGM Enhancements WG by 18 Dec 2020
Formal consultation on new and changed procedures Q1 2020
  Late Jan to April (PPC and IIR)
Consultation with GWCF on high level implementation approach
  Q2 2021
  Input to AEMO project planning
Covering
  System Capability Modelling
  Zone definition and consultation
  Training
  Readiness monitoring & reporting
  Market Trial
  Cut over approach

## Slide 31: Questions
?